## Slide 1
Validation of an Electromagnetic loop probe for Real -Time Diagnostic of Near- Field in Electrical Vehicle
Zaid Jabbar, Fabien Ndagijimana, Aktham Asfour
Univ. Grenoble Alpes, CNRS, Grenoble INP, G2Elab, 38000 Grenoble France
The loop antenna (coil) analyzed is considered to be a small compared to wavelength (< λ/10)
Impedance matching the loop antenna is done using capacitors
Transverse Electromagnetic Mode (TEM) is used for calibration
Calibration setup
TEM cell is used to create an electromagnetic field with known characteristics:
  Simplicity of the control of the specifications of the created field
  Uniform electromagnetic field inside the cell
  immunity against external electromagnetic interferences (EMI)
When the probe is positioned so that the surface of the loop is perpendicular to the Y-axis, the measurements of the AF show a strong agreement with the theoretical calculations, especially at high frequencies
When the probe is rotated 90 degrees around the Z–axis, the measurement is totally changed with respect to the theoretical calculation
Conclusion
Transversal Electromagnetic Mode (TEM)
The used loop antenna probe
13mm
13mm
Closed-circuit and square- type antenna
Small compared to the wavelength (< λ/10)
The antenna impedance is dominantly inductive (the resistive component is considered negligible)
A capacitor is thus used as a matching element to compensate the inductive reactance and match the loop impedance to 50 W
One terminal of the TEM cell is supplied with a given power from a vector network analyzer (VNA) and the other terminal is connected to a 50 Ω load
The probe is placed inside the cell and it is connected to port 2 of the VNA
The transmission coefficient S21 is measured by the VNA for the calculation of the antenna factor (AF)
Vector Network Analyzer
PORT1
PORT2
50Ω
Matching load
Center Point
Antenna Loop Probe
Results
AFth=
14th European Magnetic Sensors and Actuators Conference
Kosice-Slovakia, 24-27 June 2018
Objectives
Validation of the probe (loop antenna) used in the Near Field Scan (NFS) assessment of electric vehicles (EVs)
characterization of the loop antenna using a Transversal Electromagnetic (TEM) cell :
  determining the resulting bandwidth
  Validation of the antenna factor (AF)
The antenna factor (AF) is defined by:
Where:
Pin: input power from the VNA
Z0 : is the characteristic impedance of the TEM cell in ohms
h : height of TEM cell
Pout: measured output power of the antenna loop
S21: measured transmission coefficient
The theoretical calculation of the AF is given by
Using measurements in the TEM cell, the AF be calculated by:
Where:
HTEM: magnetic field
Vout : output voltage of the loop
  F the frequency and µ0 the permeability
Where:
Validation of the measurement method of the antenna factor (AF)
The measured antenna factor (AF) depends on the position of loop with respect to the orientation of the electromagnetic field inside the TEM cell
TEM CELL